## Slide 1: Detection of salient regions
Computer Vision Research and
Technology in eStep

## Slide 2: Computer Vision (CV)
What is it?
Why is it hard?
CV and other fields
Science and technology of machines that can see
Seeing is not perceiving
Image source: http://miracleeyegroup.com/wp-content/uploads/2014/04/Image-Processing-Domains.png

## Slide 3: CV tasks
Recognition (object)
  Detection: Where is the object?
  Classification: What is the object?
  Identification: Is the object “known”?
Motion analysis
Scene recognition
Image restoration
Images from Internet; College of the Atlantic, Maine, US.
?
?
?


## Slide 4: eStep CV research directions
State-of-the-art and niches
  Deep learning (Sherlock; MLCV group; apply in projects)
  Large Scale (within projects)
  Applications: animal/plant biometrics, digital forensics, social signal processing (within projects, pilots)
Scientific domain driven
  Where/what is my object?
  Is my object the same?
Alexander Loos, Andreas Ernst, An automated chimpanzee identification system using face detection and recognition,
EURASIP Journal on Image and Video Processing, 2013, Volume 2013, Number 1, Page 1

## Slide 5: Animal biometrics use-case
H. Kuehl and T. Burghardt. Animal biometrics: quantifying and detecting phenotypic appearance. Trends in Ecology & Evolution, 28: 432- 441, 2013.
Image from Internet

## Slide 6: Problem
Find correspondences between 2 images of the same scene/object
  Only few (up to these 2) images are available  no (deep) learning
  Images can be subject to
    geometric transformations, e.g., affine: viewpoint, scale, zoom, rotation
    Photometric transformations, e.g., blur, lighting, JPG compression
The correspondences will be used for detection or identification

## Slide 7: Salient feature detection
Saliency = interesting, distinct
Feature = “interesting” part of an image
“Manual” detection of features vs.
end-to-end learning
Types: corners (points),
edges (lines), blobs (regions)
Repeatability
Invariance to transformations

## Slide 8: MSER – best region detector
MSER = Maximally Stable Extremal Regions
Intuition
  Thresholding
,
  Area of the Connected
  Components (CC) criterion
50 81 112 143 174
2 CCs with 4-connectivity

## Slide 9: MSER – best region detector?
MSER – performing best compared to other detectors (IBR, EBR, Harris, Hessian, Salient regions...)
Shortcomings
  Sensitive to blur
  Selection criteria favors regularly shaped regions
  Overlapping redundant (too many) regions
  Performance deteriorates on high-resolution images
  Best generic, but not suited for targeted application:
  (large-scale) scientific imaging  perceptual saliency!

## Slide 10: Binary saliency
Structured  mathematical
scenes morphology
Salient structures
  Inner: holes and islands
  Boundary: indentations and protrusions
Image from Wikipedia
Structuring
Element - S
Binary Shape B
Erosion
Dilation
Opening
Closing
Hole filling
Top hat: (white); (black)
Area opening (for noise removal)

## Slide 11: Morphology-based detectors
Binary
Color  Gray  Binary
  MSSR = Morphology-based Stable Salient Regions
    Thresholding like in MSER; Binary saliency; Accumulating saliency evidence
    Only holes and islands ~ MSER+ and MSER- regions
  MSSRA = MSSR All
    All saliency types (holes, islands, indentations, protrusions)
  DMSR = Data-driven Morphology-based Salient Regions
    Single threshold from data-driven binarization
  DMSRA = DMSR All

## Slide 12: Data-driven binarization
  Single threshold
  function of the number of All, Large and Very large CCs
Example:
  Decreased lighting
  (Leuven sequence)
Otsu thresholding
Data-driven thresholding

## Slide 13: Data-driven binarization
Otsu thresholding
Data-driven thresholding
Leuven sequence images
1 and 4 (color  gray)

## Slide 14: Qualitative evaluation
D/MSSR/A are better than MSER in perceptual saliency
Original image- IBR= Intensity-Based MSER MSSRA
segmented, detail Regions

## Slide 15: Qualitative evaluation
D/MSSR/A are better than MSER in perceptual saliency
MSER DMSRA

## Slide 16: Qualitative evaluation
D/MSSR/A are better than MSER in perceptual saliency
MSER (MSER+ and MSER-) DMSR (islands only)

## Slide 17: Qualitative evaluation
D/MSSR/A are better than MSER in perceptual saliency
MSER DMSR

## Slide 18: Qualitative evaluation
DMSR detects less regions than MSER scalability at the matching step
MSER DMSR

## Slide 19: Test datasets
Oxford:
  Few sets of 6 images with increasing distortion, low resolution
  Textured and structured - real images, estimated homographies
  Transformations: viewpoint, scaling and rotation, lighting and blur
Graffiti
Boat
Leuven
Bikes

## Slide 20: Test datasets
Freiburg:
  16 sequences with higher resolution
  Real base image, generated distortions  detangle transformation from content
  Transformations: blur, lighting, rotation and zoom
Freiburg center
Cool car

## Slide 21: Test datasets
TNT:
  High resolution images: 1.5, 3, 6 and 8 MPx
  Real base image, generated transformations (viewpoint only)
Posters sequence
Transformation magnitude
1.5 MPx
6 MPx
8 MPx
3 MPx
...
...
...
...
...
...
...
...

## Slide 22: Test datasets
Too few and with drawbacks
OxFrei
  Combining features from both Oxford and Freiburg datasets
    Realistic homographies (Oxford)
    Independent transformation from content (Freiburg)
  Structured scenes
  Viewpoint, blur, lighting, scaling
  Freely available, well documented!
Small palace

## Slide 23: Performance evaluation
Number of correspondences, Nc
  Nc- # matches in common part
Repeatability score, R
  Region overlap/ error
  R = Nc / min # regions in the pair
2 matching pairs Repeatability
1 non-matching pair score: 2/3
Overlap error (usually 40%)

## Slide 24: Performance evaluation
Oxford dataset

## Slide 25: Performance evaluation
Oxfrei dataset

## Slide 26: Performance evaluation
TNT dataset

## Slide 27: Conclusions & future work
DMSR vs. MSER in structured scenes
  Worse for scale; As good as for viewpoint
  Outperforms for lighting, blur and increasing resolution
  Always less number of regions  scalable
Results submitted to ICIP 2016
MATLAB software, dataset and results available
eStep technology- detector in Python, well-tested and documented (in progress)
eStep research- use case – wood anatomy
Future research and software- matching